## Slide 1: SIMULATION OF ELECTRIC VEHICLE CHARGING
UNDER THE GUIDANCE OF
Sri. P.KRISHNA KANTH VARMA MTECH
PRESENTED BY
Y.MANISHA- 18B91A04N9
M.MOUNIKA- 19B95A0412
U.N.S.VAMSI- 19B95A0423
T.NANDA KRISHNA- 19B95A0422

## Slide 2: CONTENTS
ABSTARCT
INTRODUCTION
CAN PROTOCOL
LOG FILE
DECODED LOG FILE
OVERALL CHARGING FLOWCHART
COMPARISON BETWEEN LITHIUM ION AND LEAD ACID BATTERIES
SIGNIFICANCE OF PROBLEM
LITERATURE SURVEY
GB/T PROTOCOL

## Slide 3: Abstract
Communication among Electric Vehicle (EV), Electric Vehicle Supply Equipment (EVSE) and Battery Management System (BMS) is crucial for efficient and safe charging of an EV. To ensure safe charging process we should consider the parameters such as BMS effects, Communication between BMS and Charger i.e., GB/T protocol using CAN, by following these parameters ,we are designing an EV charger Based upon simulation.

## Slide 4: INTRODUCTION
History of EV charging technology
The first appearance of electric vehicles(EV) is started in mid-19th century.
The first EV's has disposable batteries and technology for charging was replacing dead batteries.
At the beginning of the 20th century 38% of automobiles in USA were powered by electricity. A company called General Electric introduced first charging stations called, 'Electrant'.
In late 20th century, public became more and more aware of air pollution, and idea of producing EV's started to rise again.

## Slide 5
EV CHARGER :
An EV charger, also called electric vehicle supply equipment(EVSE) is an element in EV infrastructure that supplies electric energy for recharging the electric vehicles.
EV chargers are two types Private and Public chargers
Private Charger:
The Home private chargers are generally used with 230v/15A single phase plug which can deliver an ,maximum up to about 2.5KW of power.
Public charger:
The Public Charger is a flexible and open charging station, able to charge in a standalone mode or integrated in any network with any central system.AC output from 3,7 kVA to 22 kVA
BATTERY MANAGEMENT SYSTEM
A battery management system (BMS) is any electronic system that manages a rechargeable battery(cell or battery pack), such as by protecting the battery from operating outside its safe operating area, monitoring its state, calculating Physical values such as current ,voltage and temperature from its sensors.
The major functions of BMS are to protect from over voltage, over current ,over temperature and under voltage ,to maintain voltage balance of battery cells and to estimate of internal states of battery such as State of charge(SOC),State of Health(SOH).

## Slide 6
BATTERY MANAGEMENT SYSTEM(BMS)
The major task of a battery management system (BMS) is to provide security and longevity of the battery. This can be done through continuous monitoring and control of the battery's state-of-charge (SOC) and state-of-health (SOH)

## Slide 7
STATE OF CHARGE (SOC)
The State of charge (SOC) has an important role in determining the remaining capacity of the battery pack. Accurate estimation of the SOC is very complex and difficult to implement, because of the limited battery model
The SOC of a battery is defined as the ratio of its current capacity (Q(t)) to the nominal capacity(Qn). Nominal capacity, Qn, is the maximum amount of charge that can be stored in the battery. This rating is given by the manufacturer.
SOC(t)=Q(t)/Qn
In the other words, state of charge means the ratio of the remaining charge of the battery to the total charge while the battery is fully charged at the same specific standard condition.
During charging and discharging, battery internal parameters like resistance, temperature, etc,. Vary with SOC, so these parameters are shown useful for SOC estimation. SOC is expressed in percentage.
SOC = 100% battery fully charged
SOC = 0% battery fully discharged

## Slide 8
STATE OF HEALTH (SOH)
Battery State Of Health (SOH) is an important indicator of the battery’s life. SOH reflects the ability of a battery to deliver and receive energy and power.
The SOH of a battery is defined as the ratio of its maximum instantaneous releasable capacity, (Qmax(t)) to the capacity of the new battery(Qnew).
SOH (t) = Qmax(t)/Qnew
State of Health (SOH) is a figure of merit of the present condition of a battery cell( or a battery module, or a battery system), compared to its ideal conditions.
The Soh is represented in percentage form. A SOH equal to 100% means it is a fresh/ new battery.
The SOH could be derived by capacity and the internal resistance, and it could also be derived from other battery parametres like AC impedance, self-discharging rate, and power density.

## Slide 9
A Controller Area Network(CAN) is a robust vehicle bus standard design to allow microcontrollers and device to communicate with each other applications without host computer.
It is an electronic communication bus defined by the ISO 11898 standards
The EV chargers uses 11 bit can identifiers with a default can speed of 500 Kbps.
CONTROLLER AREA NETWORK(CAN)

## Slide 10
CONTROLLER AREA NETWORK APPLICATIONS
Automotive (passenger vehicles, trucks, buses).
Electronic equipment for aviation and navigation.
Industrial automation and mechanical control.
Elevator and escalators.
Building automation.
Medical instruments and equipment.
Marine, medical, industrial, medical.

## Slide 11
Completion of physical connection
Auxiliary charging of low voltage
Charging Parameter Configuration Stage
Charging stage
Charging handshake stage
End of Charging stage
End Charging
Overall Charging Flowchart

## Slide 12: GB/T PROTOCOL
GB/T 27930 is the Chinese standard for electric vehicle battery charging. Other charging systems include the Combined Charging System (CCS) favored by European and American manufacturers, the CHAdeMO charging standard developed by a Japanese industrial consortium and Tesla’s Supercharger.
Cable charging standard GB/T 27930 is based on the SAE J1939 network protocol and uses the CAN bus with a point-to-point connection between the charger and the battery management system (BMS).
Uses the CAN Bus J1939-based protocol.
No direct connections to other can systems in the vehicle.
Nodes are identified by their addresses: - Charger: 56H - Battery Management System: F4H

## Slide 14
vcan0 1826F456 [8] 01 01 80 FF FF FF FF FF
vcan0 182756F4 [8] 70 03 00 00 00 00 00 00
vcan0 1801F456 [8] 00 01 00 00 00 44 45 4C
vcan0 1CEC56F4 [8] 10 45 00 0A 0A 00 02 00
vcan0 1CECF456 [8] 11 0A 01 FF FF 00 02 00
vcan0 1CEB56F4 [8] 01 01 01 80 08 B4 0A 53
vcan0 1CEB56F4 [8] 02 03 FF FF FF FF FF FF
vcan0 1CEB56F4 [8] 03 FF FF FF FF FF FF FF
vcan0 1CEB56F4 [8] 04 FF FF FF 4D 41 31 4C
vcan0 1CEB56F4 [8] 05 53 45 57 37 39 4A 32
vcan0 1CEB56F4 [8] 06 42 38 30 31 33 32 FF
vcan0 1CEB56F4 [8] 07 FF FF FF FF FF FF FF
vcan0 1CEB56F4 [8] 08 FF FF FF FF FF FF FF
vcan0 1CEB56F4 [8] 09 FF FF FF FF FF FF FF
vcan0 1CEB56F4 [8] 0A FF FF FF FF FF FF FF
vcan0 1CECF456 [8] 13 45 00 0A FF 00 02 00
vcan0 1CEC56F4 [8] 10 0D 00 02 02 00 06 00
vcan0 1801F456 [8] AA 01 00 00 00 44 45 4C
vcan0 1CECF456 [8] 11 02 01 FF FF 00 06 00
vcan0 1CEB56F4 [8] 01 72 01 F4 0B C7 00 70
vcan0 1CEB56F4 [8] 02 03 65 CC 02 F5 02 FF
vcan0 1CECF456 [8] 13 0D 00 02 FF 00 06 00
vcan0 1808F456 [8] E8 03 00 00 BC 02 90 01
vcan0 100956F4 [8] 00 00 00 00 00 00 00 00
vcan0 100956F4 [8] 00 00 00 00 00 00 00 00
LOG FILE :-

## Slide 15
DECODED LOG FILE :-
1826F456 01 01 80 FF FF FF FF FF CHM -- Charger handshake message
182756F4 70 03 00 00 00 00 00 00 BHM -- Battery handshake message
1801F456 00 01 00 00 00 44 45 4C CRM -- Charger recognition message
1CEC56F4 10 45 00 0A 0A 00 02 00 BRM -- Battery recognition message
1CECF456 11 0A 01 FF FF 00 02 00 CRM -- Charger requesting for BRM
1CEB56F4 01 01 01 80 08 B4 0A 53 BRM -- battery recognition message data
1CECF456 13 45 00 0A FF 00 02 00 CRM -- charger received BRM
1CEC56F4 10 0D 00 02 02 00 06 00 BCP -- charging parameters of power storage battery
1801F456 AA 01 00 00 00 44 45 4C CRM -- Charger recognition message
1CECF456 11 02 01 FF FF 00 06 00 CRM -- Charger requesting for Battery Charging Parameters of power storage battery
1CEB56F4 01 72 01 F4 0b C7 00 70 BRM -- Battery Charging Parameters data
1CECF456 13 0d 00 02 FF 00 06 00 CRM -- Charger received Battery Charging Parameters of power storage
battery
1808F456 E8 03 00 00 BC 02 90 01 CML -- charger's maximum output
100956F4 00 00 00 00 00 00 00 00 BRO -- Battery Charging Ready state
100AF456 00 FF FF FF FF FF FF FF CRO -- Charger Output Ready state
100956F4 AA 00 00 00 00 00 00 00 BRO -- Battery Charging Ready state
181056F4 EE 02 58 02 02 00 00 00 BCL -- Battery charging demand
1CEC56F4 10 09 00 02 02 00 11 00 BCS -- overall Battery Charging Status

## Slide 16: OUTPUT
CHARGER
BATTERY MANAGEMENT SYSTEM

## Slide 17: OUTPUT

## Slide 18
COMPARISON BETWEEN LITHIUM ION AND LEAD ACID BATTERIES

## Slide 19: Significance of Problem
The major concern of Battery Charging is Nonlinear charging.
And another major issue is EV charging connectors and vehicle charging parameters.
Present day consisting of different types of Electric Vehicles ,it isn’t easy to carry the chargers everywhere, thus we require more public chargers.
The public EV chargers should satisfy the different charging parameters of different EV’s.

## Slide 20: Significance of Problem
In recent times the electric vehicle explosion or accidents are decreased because of inefficient battery management system.
The next major issue in electric vehicle is heat radiated by the battery and motor.

## Slide 21: LITERATURE SURVEY
BMS MODELLING (IEEE PAPER) : From this paper we have concluded that the effect of BMS on the performance of Li-On battery module by means of charge, discharge, and frequency response.
Communication Protocols between off-Board Conductive Charger and Battery Management System for Electric vehicle, Issued by SAPR China.
SOC Estimation and BMS Design of Li-ion Battery Pack for Driving.

## Slide 22
https://youtu.be/Zz4CCAkORgY from this link we learnt how communication is done between sender and receiver using can protocol.
BMS Influence on Li-ion packs characterization and Modeling.

## Slide 23
Click to add text